Power with No Fiber: -54.05 dBm

Power with Control Fiber: +02.25 dBm

C1: Control fiber 1, is labeled as C1. It has a 2.5mm ferrule on one end and a 1.25mm ferrule on the other
C2: Control fiber 1, is labeled as C2. It has a 2.5mm ferrule on one end an a 1.25mm ferrule one the other.

C1 + C2:	Power Received (dBm)
Trial 1	+01.54
Trial 2	+1.82
Trial 3	+1.87
Trial 4	+1.58
Trial 5	+1.68
Trial 6	+1.86
Trial 7	+1.75
Trial 8	+1.20
Trial 9	+1.60
Trial 10	+1.68
Average	+1.658

C1+3+C2	Power Received (dBm)

Trial 1	+1.35
Trial 2	+1.40
Trial 3	+1.16
Trial 4	+0.8
Trial 5	+0.71
Trial 6
Trial 7
Trial 8
Trial 9
Trial 10
Average

C1+3+C2	Power Received (dBm)

Trial 1	+1.35
Trial 2	+1.40
Trial 3	+1.16
Trial 4	+0.8
Trial 5	+0.71
Average	1.08

**C3: new control fiber after C2 broke. C3 is less polished than C2 so loss should be expected to be lower.
Note: Twisting the 2.5mm ferrules in the light input and output seems to make a significant difference in loss. Example, twisting made dBm go from 0.64dB in trial 3 to 1.05dB in trial 4.

C3+C1	Power Received (dBm)

Trial 1	+1.14
Trial 2	+0.94
Trial 3	+0.64
Trial 4	+1.05
Trial 5	+0.95
Trial 6	+0.87
Trial 7	+1.07
Trial 8	+1.03
Trial 9	+0.92
Trial 10	+1.03

C3 + Fiber in tube and actuator(random fiber selected #1) + C1:
*Trial 1 to trial 2 I twisted the white connector and more red light was visibly escaping it. How the connector is positioned matters.

C3+fiber in tube#1 +C1	Power Received (dBm)

Trial 1	+1.12
Trial 2	-0.245
Trial 3	+1.04
Trial 4	+0.93
Trial 5	+1.02
Trial 6	+0.87
Trial 7	+1.00
Trial 8	+1.09
Trial 9	+0.94
Trial 10	+0.93
Average

C3 + Fiber in tube and actuator(random fiber selected#2) + C1:
Notes for below:
I think the fiber in the plastic sleeve of connector 1 might have broken a bit. I could see light coming through. I think this signifies that the fibers not being bent or strained is important for optimal light

C3+fiber in tube #2 +C1	dB

Trial 1	+0.84
Trial 2	+1.01
Trial 3	+0.90
Trial 4	+0.93
Trial 5	+0.60
Trial 6	+0.92
Trial 7	+0.73
Trial 8	+1.09
Trial 9	+0.94
Trial 10	+0.43
Average